M3 Battery SPI Capture Log.

Setup :
HV Controller and one slave on “batman” with 25 lifepo4 cells.

Salea Logic 8 on “batman” spi bus at 24mhz , 3 second window. Spi decode active. SPI mode 3.

Captures :

1)All cells connected. Min : 3.268v , Max 3.279 , temps : 18c

2)Cell 1 replaced with psu. Min : 2.662v , Max 3.886 , temps : 18c

3)Cell 1 replaced with psu. Min : 2.444v , Max 4.104 , temps : 18.5c

4)Cell 1 replaced with psu ,temps : 18.5c, 2 sweeps of psu from 0.5-5v during capture.

5)All cells connected. Min : 3.264v , Max 3.714, temps : 18.5c, psu charging cell 24.

6)All cells connected. Min : 3.22v , Max 3.308 , temps ramped from 25 to 26c during capture.